## Slide 1: OFS ASP – Multi-Link Support Douglas Groen

## Slide 2: Overview
Increasing PCIe link speeds led the FIM to implement 2 separate interfaces to the AFU
  Physical interfaces: 2 x Gen5x8 instead of 1 x Gen5x16
  On-chip interfaces: 2 x 512 bit @ 500 MHz instead of either 1 x 1024 bit @ 500 MHz or 1 x 512 bit @ 1GHz
OPAE supports this already, and there are example RTL designs here:
  https://github.com/OFS/examples-afu/tree/main/tutorial/afu_types/04_multi_link

## Slide 3: Goals for ASP Support
Minimize changes to ASP mmd software
  None were required – mmd doesn’t know how many links exist
DMA controller must leverage both links
  Autonomously split a transfer across both links
USM / kernel must leverage both links
  Explicit access of two ‘global_mem’ interfaces
Share as many VTP resources as possible
  Same address-space on the host, no need to duplicate all VTP resources

## Slide 4: High-Level ASP Changes
New board variant at the top level of the repo
Arrays of SystemVerilog interfaces to enable parameterization
Replication of module instances using generate
New `defines to enable changes to the kernel-system’s port-list
Updates to board_spec.xml for the USM variant
  new global_mem interface for 2nd USM channel
  address-range updates for the DDR interfaces

## Slide 5: Changes to DMA Controller
No changes needed in mmd – the same 3 registers are used to define a DMA transfer: source address, destination address, transfer length
DMA ‘dispatcher’ module changes
  Logic to split a DMA transaction into 2 halves
  Logic to detect transfer completion and send IRQ or message to mmd
DMA ‘data-transfer’ modules are duplicated to support each half of the total transaction
MMIO transactions occur only on the parent PCIe link
  DFH reading, status/control registers, H2F IRQ, F2H ‘magic number’, etc

## Slide 6: Changes to USM Channels
Duplicate RTL paths for USM[0] and USM[1] from the kernel-system, through pipeline bridges, to VTP translation blocks
The USM test within boardtest was modified to explicitly leverage both channels
  https://github.com/DouglasGroen/oneapi-asp/tree/2link_docs/iseries-dk_2link/docs/oneAPI-samples/boardtest
  No complicated changes to the ASP for this – mainly duplication of code (in generate blocks) to support the new channel

## Slide 7: Changes to VTP Connections
No changes needed in mmd – the mmd doesn’t know there are multiple links
The host-memory space is common across both of the PCIe interfaces, which means we can use a single VTP-service block on the parent MMIO link
Add new VTP-translation modules for the new links
  Increase the number of vtp_port interfaces such that each DMA and USM VTP-translation module has 2 ports
Link 0 (the parent link) will carry the same traffic it used to carry
  Normal MMIO transactions, DMA[0] and USM[0] traffic, VTP services
Link 1 (the child link) will only carry DMA[1] and USM[1] traffic (and a very basic child-DFH response)